## Slide 1: Lab 1 Update
2.22.21
Kylie Outlaw & Maria Abbasi

## Slide 2: Loop Timing
Task #4 Implementation
TIM2 on PA0
  Count-up timer
  Period of 100,000
  Pre-scalar of 83
Every clock tick is 1 microsecond
Struct objects used to keep track of different loops’ timing
  Total elapsed time stored using a uint32_t
  Number of loops tracked using a uint16_t counter
    Averages based on 65,535 consecutive loop timings for inner/outer loops
    Averages based on 30 consecutive loop timings for the blink loop

## Slide 3: Loop Timing
Task #4 Implementation
New “Loop_timer.h” and “Loop_timer.c” files
Holds data and functions for the “loop_timer” struct
  Init, begin, stop, reset, print functions
  Start tick
  End tick
  Total time
  Number of loops completed
Each loop is measured using a uint16_t counter
  Averages based on 65,535 consecutive loop timings

## Slide 4: Loop Timing
- Adjusted the main.c calibration to test TIM2 ticks.
- Looking at the output, 1000 clock ticks match 1 HAL tick .
      - HAL tick is set up by the system so that each tick is 1ms, or 1/1000 of the processor clock speed.
- The inner loop and outer loops are timed automatically in the code and the average runtimes are output to COM3.
- The inner loop runs at 1.0us average.
- The outer loop runs at 1.2us average.
- The blink loop runs at 1001.00ms, or 1.001s on average.
- This is slightly higher than expected.
Image: COM3 output

## Slide 5: Scheduler Priority

## Slide 6: Current Schedule Priority
Sch_basic.c -> sch_loop()
  Polled tasks – checks tasks in loop for hardware interrupt conditions
  First scheduled, first executed
  ADC ➡ UART Rx ➡UART Tx

## Slide 7: Current Schedule Priority
Tasks_lab_1.c -> timer_cb_text#()
  Timeout tasks
  Based on tick timeout, software-enabled interrupt
  Higher priority than polling loop
  Every ~1s LED toggles

## Slide 8: Scheduling Approach
Asynchronous events handled by hardware interrupts
Synchronous events / periodic tasks handled by software interrupts
  Earliest Deadline First
Scheduling approach you plan to implement
Data structures needed for implementations
  What info needed about the application, tasks (e.g. deadline??)
  Identify context you are considering – specific application – to help select numbers (periods, deadlines, etc.), make design decisions
Describe how you intend to use peripherals and interrupts

## Slide 9: Scheduling Approach
Asynchronous events handled by hardware interrupts
Synchronous events / periodic tasks handled by software interrupts
  Earliest deadline first
Submit a presentation that:
Summarize timing results (e.g. table, plot)
Scheduling approach you plan to implement
Data structures needed for implementations
  What info needed about the application, tasks (e.g. deadline??)
  Identify context you are considering – specific application – to help select numbers (periods, deadlines, etc.), make design decisions
Describe how you intend to use peripherals and interrupts

## Slide 10: YOU CAN ALSO SPLIT YOUR CONTENT
White
Is the color of milk and fresh snow, the color produced by the combination of all the colors of the visible spectrum.
Black
Is the color of ebony and of outer space. It has been the symbolic color of elegance, solemnity and authority.

## Slide 11: IN TWO OR THREE COLUMNS
Yellow
Is the color of gold, butter and ripe lemons. In the spectrum of visible light, yellow is found between green and orange.
Blue
Is the colour of the clear sky and the deep sea. It is located between violet and green on the optical spectrum.
Red
Is the color of blood, and because of this it has historically been associated with sacrifice, danger and courage.

## Slide 12: EXTRA GRAPHICS

## Slide 13
SlidesCarnival icons are editable shapes.
This means that you can:
Resize them without losing quality.
Change line color, width and style.
Isn’t that nice? :)
Examples:

## Slide 14: Diagrams and infographics

## Slide 15
Now you can use any emoji as an icon!
And of course it resizes without losing quality and you can change the color.
How? Follow Google instructions https://twitter.com/googledocs/status/730087240156643328
✋👆👉👍👤👦👧👨👩👪💃🏃💑❤😂😉😋😒😭👶😸🐟🍒🍔💣📌📖🔨🎃🎈🎨🏈🏰🌏🔌🔑 and many more...
😉