## Slide 1: Lab 1 Update
2.24.21
Kylie Outlaw & Maria Abbasi

## Slide 2: Loop Timing
Task #4 Implementation
TIM2 on PA0
  Count-up timer
  Period of 100,000
  Pre-scalar of 83
Every clock tick is 1 microsecond
Struct objects used to keep track of different loops’ timing
  Total elapsed time stored using a uint32_t
  Number of loops tracked using a uint16_t counter
    Averages based on 65,535 consecutive loop timings for inner/outer loops
    Averages based on 30 consecutive loop timings for the blink loop

## Slide 3: Loop Timing
Task #4 Implementation
New “Loop_timer.h” and “Loop_timer.c” files
Holds data and functions for the “loop_timer” struct
  Init, begin, stop, reset, print functions
  Start tick
  End tick
  Total time
  Number of loops completed
Each loop is measured using a uint16_t counter
  Averages based on 65,535 consecutive loop timings

## Slide 4: Loop Timing
- Adjusted the main.c calibration to test TIM2 ticks.
- Looking at the output, 1000 clock ticks match 1 HAL tick .
      - HAL tick is set up by the system so that each tick is 1ms, or 1/1000 of the processor clock speed.
- The inner loop and outer loops are timed automatically in the code and the average runtimes are output to COM3.
- The inner loop runs at 1.0us average.
- The outer loop runs at 1.2us average.
- The blink loop runs at 1001.00ms, or 1.001s on average.
- This is slightly higher than expected.
Image: COM3 output

## Slide 5: Scheduler Priority

## Slide 6: Current Schedule Priority
Sch_basic.c - sch_loop()
  Polled tasks – checks tasks in loop for hardware conditions
  First scheduled, first checked, first executed
  ADC ➡ UART Rx ➡UART Tx

## Slide 7: Current Schedule Priority
Tasks_lab_1.c - sch_create_timeout()
  Based on tick timeout
  Higher priority than polling loop
  Every ~1s LED toggles

## Slide 8: Scheduling Approach
Asynchronous events handled by hardware interrupts
  HAL_GPIO_EXTI_Callback();
  Break tasks into priority groups
    HAL_NVIC_SetPriority() : 0 to 15
    If multiple asynchronous interrupts occur at same time, highest priority gets completed first

## Slide 9: Scheduling Approach
Synchronous events / periodic tasks handled by timer interrupts
  Set up timer with interrupt at each period time
  Set HAL_TIM_Period_ElapsedCallback() to process
  Will need the period of all synchronous / periodic tasks

## Slide 10: Questions?